EMERGENCY TOWING BOOKLET

Volume A

Table of Communicating Information

(Information to be provided to a towing company)

XXX Marine Transportation Ltd.

| 3 |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2 |  |  |  |  |  |  |  |  |
| 1 |  |  |  |  |  |  |  |  |
| 0 |  |  |  |  |  |  |  |  |
| Rev. | Date | Description of Revision | Prepared | Checked | Approved |

Table of Information (1/2)

| No. | Item | Current status |
| --- | --- | --- |
| (1) | Present time | Day/Month/Year | Time |
|  |  | 10/10/08 | JST | 12:30 |
| (2) | Current position | 200km off Choshi 36ﾟ59'48"N 142ﾟ25'31"E |
| (3) | Cause of requesting towage | Loss of navigability due to the breakage of the crankshaft of No.2 main engine |
| (4) | Weather conditions | Cloudy |
| (5) | Wind velocity and direction | Velocity (m/s) | Direction |
|  |  | About 10 | Northeast |
| (6) | Wave height | about 1.5 | (m) |
| (7) | Weather forecast | The typhoon is approaching and wind is expected to become stronger. |
| (8) | Drifting speed and direction | Speed (kt) | Direction |
|  |  | About 1.0 | Southwest |
| (9) | Imminent danger (e.g. grounding) (if any, describe the expected danger) |  | Note: There is no grounding risk now, but there is a possibility to approach to the land in 4 days with this drifting situation. |
| (10) | Flooding (if any, describe the status) |  | Status : |
| (11) | Cargo (if any, describe the type) |  | Note : Grain |
| (12) | Fore draft | 10.6 | (m) |
| (13) | Aft draft | 11.4 | (m) |

Table of Information (2/2)

| No. | Item | Current status |
| --- | --- | --- |
| (14) | Can be towed from the bow? |  | Status : |
| (15) | Can use power on board? |  | Status : |
| (16) | Can use deck lighting for the towing line connection? |  | Status : |
| (17) | Can use the mooring winch for winding the towing line? |  | Status : |
| (18) | Can use the mooring equipment on the deck for the towing line connection? |  | Status : |
| (19) | Can use towing lights (side lights, stern lights)? |  | Status : |
| (20) | Ready to display the black diamond? |  | Status : Under preparation |
| (21) | Can use the rudder (describe the status)? |  | Status : No problem |
| (22) | If the rudder is damaged, what is the current rudder angle and is it possible to return to midship? |  | Status : No problem |
| (23) | Can use the main engine? |  | Status : |
| (24) | Can control the trim? |  | Status : Trim by stern at present |
| (25) | Is there heeling? |  | Status : |
| (26) | How to prevent free propeller rotation? | Now, we're working to connect the coupling bolts of the intermediate shaft bearing with hull. It will be finished within two hours. |
| (27) | Oil leakage from the stern tube (if any, describe the status) |  | Status : |

Emergency Towing Booklet

Volume B

Text

XXX Marine Transportation Ltd.

| 3 |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2 |  |  |  |  |  |  |  |  |
| 1 |  |  |  |  |  |  |  |  |
| 0 |  |  |  |  |  |  |  |  |
| Rev. | Date | Description of Revision | Prepared | Checked | Approved |

Contents

Page

1.  Main particulars                                    	-------------------------------------        		6

2.  List of facilities                                        -------------------------------------    	6

2.1   List of communication equipment　　		-------------------------   	6

2.2   List of power supply equipment           		-------------------------        	6

2.3   Steering gears                                       			-------------------------     	6

2.4   Anchors, chain cables and mooring ropes                               ----------    	7

2.5   Arrangement of deck facilities on upper deck in the bow       ----------     	8

2.6   Arrangement of deck facilities on upper deck in the stern      ----------     	9

2.7   List of deck tools                                  			-------------------------     	10

2.8   List of other facilities                           			-------------------------    	10

3.  Decision matrix for determining towing patterns           -------------------     	11

4.  Towing patterns                             		-------------------------------------     	12

(1)Pattern1-F (towing from the bow)        		-------------------------------------     	12

(2)Pattern1-A (towing from the stern)      		-------------------------------------	12

(3)Pattern2-F (towing from the bow)       	-------------------------------------		13

(4)Pattern2-A (towing from the stern)     	-------------------------------------	13

(5)Pattern3-F (towing from the bow)        	-------------------------------------	14

(6)Pattern3-A (towing from the stern)      	-------------------------------------	14

5.  Organization                                           			-------------------------     	15

5.1   Personnel distribution                                     	-------------------------    	15

5.2   List of tasks and necessary equipment           	-------------------------     	16

5.3 Notes for the towing operation                         	-------------------------     	17

6. Examples of the procedures for connecting towing lines     ---------------     	17

(1)Pattern1-F: Use a wire rope                   			-------------------------           18

(2)Pattern2-F: Use wire ropes                    			-------------------------     	21

(3)Pattern3-F: Use hawsers of the ship      			-------------------------     	24

1. Main particulars

| (1) | Ship's name |  |
| --- | --- | --- |
| (2) | Call sign |  |
| (3) | IMO number |  |
| (4) | Type of ship | Panamax BC |
| (5) | Principal dimensions | Loa=225m |
|  |  | Lpp×B×D=217m×32.2m×19.15m |
| (6) | Height of mooring deck above keel | Bow : 21.75m |
|  |  | Stern : 19.96m |
| (7) | Draft and displacement at full load condition | Draft : 13.85m |
|  |  | Displacement : 84,000MT |
| (8) | Draft and displacement at light ballast condition | Draft : 5.6m |
|  |  | Displacement : 31,000MT |

2. List of facilities

2.1 List of communication equipment

| No. | Name | Particulars |
| --- | --- | --- |
| (1) | Inmalsat B | Phone number (3○○○○○○○○) |
| (2) | Inmalsat C | Phone number (4○○○○○○○○) |
| (3) | Wireless radio | 1-MF/HF radio station |
| (4) | Wireless radio | 3-two-way VHF radio telephone |
| (5) | International VHF | 1-main VHF radio telephone |
| (6) | International VHF | 1-auxiliary VHF radio telephone |
| (7) | Maritime telephone | Phone number ( ) |
| (8) | Portable wireless radio | 5-Portable transceiver of 400MHz band,F3,1W |

2.2 List of power supply equipment

| No. | Name | Location | Particulars |
| --- | --- | --- | --- |
| (1) | Main generator | In engine room | D/G×3 : 400kw each |
| (2) | Emerg. generator | In engine casing on port side | E/G×1 : 99kw |
| (3) | Portable generator |  | None |
| (4) | Battery for gen. use | In battery room on aft navig'n deck | 1-DC 28V×200Ah,10hrs discharge |
| (5) | Do. for radio equip. | Do. | 1-DC 24V×200Ah,10hrs discharge |
| (6) | Do. for emerg. gen. | Do. | 1-DC 24V,20hrs discharge |
| (7) | Shore connection | On ESB in emerg. generator room (in engine casing on portside of upper deck) | Supplied to pump units for deck machineries |

2.3 Steering gears

| No. | Name | Particulars |
| --- | --- | --- |
| (1) | Steering gear | Piston type P-80, Pump unit : 18.5kw×2 |
| (2) | Emerg.steering gear |  |
| (3) | Power source for (2) | Emergency generator |

  - Anchors, chain cables and mooring ropes

| No. | Name | Particulars | SWL(kN) |
| --- | --- | --- | --- |
| (1) | Bower anchor | Stockless high holding power type |  |  |
|  |  | AC-14 |  |  |  |  |  |
|  |  | 2-7875㎏ |  |  |  |  |  |
|  |  | 2-anchor shackle with taper pin |  |  |
| (2) | Chain cable | Extra high strength flash butt-welded steel with welded stud at both ends | 4300 |
|  |  | (Grade 3) |  |  |  |  |  |
|  |  | Kenter joining shackle (every 55m) |  |  |
|  |  | 2-φ78×330m |  |  |  |  |
| (3) | Mooring rope | 6-φ62×220m |  |  |  | 570 |
|  |  | Polypropylene rope |  |  |  |  |
|  |  | (8 Strand) |  |  |  |  |
| (4) | Chain cable stopper | Roller bar type |  |  |  |  |

2.5 Arrangement of deck facilities on upper deck in the bow

| No. | Name (deck machineries) | Particulars |
| --- | --- | --- |
| (F-1P) | Windlass & mooring winch | Wheel | Gypsy wheel 289kN×9m/min |  |
|  |  |  | Chain SWL 4300kN 78mm×330m |
|  |  | P-Rope drums | 125kN×15m/min |  |  |
|  |  |  | Rope SWL 570kN 62mmx220m |
|  |  | S-Rope drums | 125kN×15m/min |  |  |
|  |  |  | Rope SWL 570kN 62mmx220m |
|  |  | Hydro power unit | 99kw×3 |  |  |  |
| (F-1S) | Windlass & mooring winch | Wheel | Gypsy wheel 289kN×9m/min |  |
|  |  |  | Chain SWL 4300kN 78mm×330m |
|  |  | P-Rope drums | 125kN×15m/min |  |  |
|  |  |  | Rope SWL 570kN 62mmx220m |
|  |  | S-Rope drums | 125kN×15m/min |  |  |
|  |  |  | Rope SWL 570kN 62mmx220m |
|  |  | Hydro power unit | 99kw×3 |  |  |  |

| No. | Name (deck fittings) | Particulars | SWL(kN) |
| --- | --- | --- | --- |
| (F-2P) | φ355 Bollard | JIS F2001-355 | 510 |
| (F-2S) | φ355 Bollard | JIS F2001-355 | 510 |
| (F-3P) | φ355 Bollard | JIS F2001-355 | 510 |
| (F-3S) | φ355 Bollard | JIS F2001-355 | 510 |
| (F-4P) | φ355 Bollard | JIS F2001-355 | 510 |
| (F-4S) | φ355 Bollard | JIS F2001-355 | 510 |
| (F-5P) | φ300×2 Rollers fairleader | JIS F2014 AF-300 | 824 |
| (F-5S) | φ300×2 Rollers fairleader | JIS F2014 AF-300 | 824 |
| (F-6P) | φ300×3 Rollers fairleader | JIS F2014 CF-300 | 824 |
| (F-6S) | φ300×3 Rollers fairleader | JIS F2014 CF-300 | 824 |
| (F-7C) | 360×260 Panama chock | JIS F2017 BC360 | 686 |
| (F-8P) | 360×260 Panama chock | JIS F2017 AP360 | 686 |
| (F-8S) | 360×260 Panama chock | JIS F2017 AP360 | 686 |

2.6 Arrangement of deck facilities on upper deck in the stern

| No. | Name (deck machineries) | Particulars |
| --- | --- | --- |
| (A-1P) | Mooring winch | Fore-Rope drums | 125kN×15m/min |  |  |
|  |  |  | Rope SWL 570kN 62mmx220m |  |
|  |  | Aft-Rope drums | 125kN×15m/min |  |  |
|  |  |  | Rope SWL 570kN 62mmx220m |  |
| (A-1S) | Mooring winch | Fore-Rope drums | 125kN×15m/min |  |  |
|  |  |  | Rope SWL 570kN 62mmx220m |  |
|  |  | Aft-Rope drums | 125kN×15m/min |  |  |
|  |  |  | Rope SWL 570kN 62mmx220m |  |

| No. | Name (deck fittings) | Particulars | SWL(kN) |
| --- | --- | --- | --- |
| (A-2P) | φ355 Bollard |  |  | JIS F2001-355 |  |  | 510 |
| (A-2S) | φ355 Bollard |  |  | JIS F2001-355 |  |  | 510 |
| (A-3P) | φ355 Bollard |  |  | JIS F2001-355 |  |  | 510 |
| (A-3S) | φ355 Bollard |  |  | JIS F2001-355 |  |  | 510 |
| (A-4P) | φ355 Bollard |  |  | JIS F2001-355 |  |  | 510 |
| (A-4S) | φ355 Bollard |  |  | JIS F2001-355 |  |  | 510 |
| (A-5P) | φ300×2 Rollers fairleader |  | JIS F2014 AF-300 |  | 824 |
| (A-5S) | φ300×2 Rollers fairleader |  | JIS F2014 AF-300 |  | 824 |
| (A-6P) | φ300×2 Rollers fairleader |  | JIS F2014 AF-300 |  | 824 |
| (A-6S) | φ300×2 Rollers fairleader |  | JIS F2014 AF-300 |  | 824 |
| (A-7P) | φ300×2 Rollers fairleader |  | JIS F2014 AF-300 |  | 824 |
| (A-7S) | φ300×2 Rollers fairleader |  | JIS F2014 AF-300 |  | 824 |
| (A-8P) | φ300×3 Rollers fairleader |  | JIS F2014 CF-300 |  | 824 |
| (A-8S) | φ300×3 Rollers fairleader |  | JIS F2014 CF-300 |  | 824 |
| (A-9C) | 360×260 Panama chock |  | JIS F2017 AP360 |  | 686 |
| (A-10P) | 360×260 Panama chock |  | JIS F2017 AP360 |  | 686 |
| (A-10S) | 360×260 Panama chock |  | JIS F2017 AP360 |  | 686 |
| (A-11P) | 310×230 Panama chock |  | JIS F2017 AP310 |  | 686 |
| (A-11S) | 310×230 Panama chock |  | JIS F2017 AP310 |  | 686 |

2.7 List of deck tools

| No. | Name | Particulars |
| --- | --- | --- |
| (1) | Stopper chain or strop chain |  |  |  | 2 pieces |  |
| (2) | Shackle for the above and sling wire for connecting hawser |  | 2 sets |  |
| (3) | Sledgehammer, bar, hand hammer and knife |  | 1 piece each |
| (4) | Stopper rope |  |  |  |  | 20㎜×20m |
| (5) | Pin punch for joining shackle |  |  |  |  |  |  |  |
| (6) | Seizing wire or sprit pin |  |  |  |  |  |  |  |
| (7) | Life line throwing apparatus |  |  |  |  |  |  |  |

2.8 List of other facilities

| No. | Name and Particulars |
| --- | --- |
| Cargo handling gears |
| (1) | 1-Electric motor driven traveling crane for handling engine parts and provisions |
|  | Hoisting : 29.4kN×abt.12m/min |  |  |  |  |
|  | Traveling speed : abt.15m/min |  |  |  |  |  |
|  | Location : on upper deck between accommodation and engine casing |  |  |  |  |
| (2) | 2-Steel davit for handling Suez boat & fuel oil hoses |  |  |
|  | Hoisting : 39.2kN by air motor winch |  |  |  |  |
|  | Slewing : Manually operated slewing gear |  |  |  |
|  | Location : on upper deck in front of accommodation |  |  |
| (3) | 1-200㎏chain block for Suez search light in the bow |  |  |
| Access Ladders |
| (4) | 2-Accommodation ladder operated by electric motor winch |  |  |
|  | Location : on upper deck at accommodation |  |  |  |
| (5) | 1 - Portable rope ladder |  |  |  |  |  |
|  | Location : on upper deck in midship |  |  |  |  |
| (6) | 2-Short accommodation ladders operated by air motor winch |  |  |
|  | Location : on upper deck in midship |  |  |  |  |

3. Decision matrix for determining towing patterns

The towing pattern should be decided by the captain of the ship, in consultation with the captain of the towing ship, by referring the following Decision Matrix. In considering the towing pattern, the ship status and the surrounding conditions (e.g. weather conditions, availability of the propulsion system and of power supply for deck machinery and imminent danger of grounding) should be taken into account.

The primary towing patterns should be to tow from the bow. If it is not possible to tow from the bow for some reasons such as collision, towing from the stern may be selected as an alternative.

| Condition | Towing pattern | Remarks |
| --- | --- | --- |
|  | f/m the bow | f/m the stern |  |
| In case there is imminent danger such as grounding in a short time; less than 1 hour for instance. | 1-F | 1-A | ●In case the towing ship has the sufficient towing force, ①The pattern 2 (2-F or 2-A) should be taken, if it is necessary to distribute the towing force into two lines. ②However, when there is not enough time to make arrangements for the pattern 2, the pattern 1 may be taken on the condition that the towing force is controlled not to exceed the strength of the deck fittings. ③Furthermore, at the later stage, the towing pattern 1 should be changed to the pattern 2 when there is enough time to do so. |
| In case the weather is bad when connecting the towing lines between the ship and the towing ship | 1-F | 1-A | ●In case the towing ship has the sufficient towing force, ①The pattern 2 (2-F or 2-A) should be taken, if it is necessary to distribute the towing force into two lines. ②However, when making arrangements for the pattern 2 may cause danger due to the bad weather, the pattern 1 may be taken on the condition that the towing force is controlled not to exceed the strength of the deck fittings. ③Furthermore, at the later stage, the towing pattern should be changed to the pattern 2 when the weather improves. |
| In case there is no power supply for deck machinery to handle the towing lines. | 1-F | 1-A | ●In case the towing ship has the sufficient towing force, ①The pattern 2 (2-F or 2-A) should be taken, if it is necessary to distribute the towing force into two lines. ②However, when there is no choice but to take the pattern 1 for unavoidable reasons, the towing force should be controlled not to exceed the strength of deck fittings. |
| In case the duration of being towed is long; more than 1 day for instance. | 2-F | 2-A | ●If possible, chain should be used. |
| In case towing apparatus is not supplied from the towing ship. | 3-F | 3-A | ●The mooring hawser or other towing lines of the ship should be passed to the towing ship. |

4. Towing patterns

The towing patterns for this ship are the following 6 patterns in principle.

The pattern is determined by the captain or the headquarters in consultation with the towing company, taking into account of the ship status and the surrounding conditions.

(1)Pattern1-F (towing from the bow)

Use a hawser or a wire rope and a bollard

(2)Pattern1-A (towing from the stern)

Use a hawser or a wire rope and a bollard

(3)Pattern2-F (towing from the bow)

Use wire ropes or chains and two bollards in order to distribute the towing force

(4)Pattern2-A (towing from the stern)

Use wire ropes or chains and two bollards in order to distribute the towing force.

For this ship, however, in case it is difficult to distribute the towing force into two bollards due to the mooring arrangement as shown below, it is required to reinforce the fittings and/or install a towing bracket by workers of either the towing ship or this ship.

(5)Pattern3-F (towing from the bow)

Use hawsers of the ship

(6)Pattern3-A (towing from the stern)

Use hawsers of the ship

5. Organization

5.1   Personnel distribution

The towing operation should be conducted in accordance with the following organization chart.

5.2 List of tasks and necessary equipment

The following table shows the responsibilities of each crew and the necessary equipment for the towing operation. Bosun should have deck tools (refer to 2.7 Table of deck tools) prepared and provide crews with tools.

| Title | Duty | Necessary equipment |
| --- | --- | --- |
|  |  | Life saving equipment | Portable wireless radio | on-deck tool |
| Chief officer | Chief person on deck |  | ○ | ○ | × |
| 2nd officer | Assistant to chief officer |  | ○ | ○ | × |
| 2nd engineer | Assistant to chief officer |  | ○ | ○ | × |
| Bosun | Leader on deck directing work to members | ○ | ○ | × |
| Seaman A | Operator of mooring winches |  | ○ | × | ○ |
| Seaman B | Handling ropes |  |  | ○ | × | ○ |
| Seaman C | Do. |  |  |  | ○ | × | ○ |
| Fireman A | Do. |  |  |  | ○ | × | ○ |
| Fireman B | Do. |  |  |  | ○ | × | ○ |
| Fireman C | Do. |  |  |  | ○ | × | ○ |

5.3 Notes for the towing operation

(1)During the connecting operation

①All the crews should be well informed of the work procedures and personnel distribution.

②The person in charge of the work (chief officer) on F'cle deck (or Poop deck) should always contact the captain, and finish the work as fast as possible.

③The person in charge of the work should watch the movement of towing ship carefully. When the towing line with eye splice is strained, he should evacuate the crews to safe places.

(2)During towing operation

①It is necessary to grease up continuously in order to prevent wear of ropes in Panama chock when wire ropes are used as towing lines.

②Wear-out condition in Panama chock should be constantly checked.

③Rudder should be operated to improve the ship's movement of following to the towing ship, if necessary.

④It should be confirmed in the engine room if there is a problem of free propeller rotation.

It is necessary to determine in advance how to lock the propeller shaft.

6. Examples of the procedures for connecting towing lines

As examples of the procedures for connecting towing lines, the basic procedures for the pattern 1-F, 2-F and 3-F are shown below. The captain should decide the connecting procedures in consideration of the arrangement of mooring equipment and the ship status after consulting with the captain of the towing ship and inform the crews of the procedures.

(Note: The following examples are developed to be used as the common procedures for ordinary ships. It should be noted, however, that the examples are developed for this ship and that there may be cases where these examples are not applicable to other ships, especially of which design and equipment are largely different from this ship. Showing the connecting procedures simply by diagrams of deck arrangements used in Section 2.5 and Section 2.6 may be a practical way.)

(1)Pattern1-F: Use a wire rope

(10) Make sure the wire with eye splice does not touch the corner of any structures. Take in the slack by pounding with a sledgehammer so that the wire in the bollard is lowered as much as possible.

(11) Lubricate the wire with eye splice with grease where it is rubbed with the Panama chock and finish the connecting operation.

(2)Pattern2-F: Use wire ropes

(10) Make sure the wire with eye splice does not touch the corner of any structures. Take in the slack by pounding with a sledgehammer so that the wire in the bollard is lowered as much as possible.

(11) Lubricate the wire with eye splice with grease where it is rubbed with the Panama chock and finish the connecting operation.

(3)Pattern3-F: Use hawsers of the ship

(5) Adjust winches so that the tension of both sides becomes approximately the same extent and make sure that the hawsers do not touch the corners of any structures.

Then, disengage the clutches and apply brakes of the winches, and finish the connecting operation.

# Footnotes

JIS : Japanese Industrial Standard

# Text boxes

□Yes   □No

ﾚ

□Yes   □No

ﾚ

□Yes   □No

ﾚ

□Yes   □No

ﾚ

□Yes   □No

□Yes   □No

ﾚ

□Yes   □No

□Yes   □No

□Yes   □No

ﾚ

□Yes   □No

ﾚ

□Yes   □No

□Yes   □No

ﾚ

ﾚ

ﾚ

An Example of

Panamax Bulk Carrier

ﾚ

ﾚ

□Yes   □No

ﾚ

□Yes   □No

ﾚ

□Yes   □No

ﾚ

□Yes   □No

An Example of

Panamax Bulk Carrier

(1) Pull out the hawser from the starboard side hawser reel of the port side mooring winch.

(2) Receive the messenger rope from the towing ship.

(3) Pass the messenger rope through the Panama chock and the bollard, and wind it up in the starboard side hawser reel of the port side mooring winch.  Make sure the rope is not rubbed with the corner of bulwark stay near the Panama chock.

Procedure (1), (2) & (3)

(4) Raise the wire with eye splice connected with the messenger rope to upper deck in the bow through the Panama chock by winding the starboard side hawser reel of the port side mooring winch, and stop the winch.  Wind up the messenger rope in the wire hawser reel of the port side mooring winch so that the eye splice at the end of the wire can be hooked on the bollard.

Procedure (4)

Procedure (5) & (6)

5) Wind off the hawser from the port side hawser reel of the port side mooring winch and connect it to the wire with eye splice through the roller fairleader by using the strop chain.

(6) Wind up the hawser in the port side hawser reel of the port side mooring winch and keep the tension on the middle of the wire with eye splice.

(7) Wind off the starboard side hawser reel of the port side mooring winch and separate the wire with eye splice from the messenger wire.

Procedure (7)

(8) Hook the eye splice at the end of the wire on the bollard.

Procedure (8)

(9) Wind off the port side hawser reel of the port side mooring winch and detach the strop chain from the wire with eye splice.

Procedure (9)

(1) Pull out the hawser from the starboard side hawser reel of the port side mooring winch.

(2) Receive the messenger rope from the towing ship.

(3) Pass the messenger rope through the Panama chock and the bollard, and wind it up in the starboard side hawser reel of the port side mooring winch.  Make sure the rope is not rubbed with the corner of bulwark stay near the Panama chock.

Procedure (1), (2) & (3)

Procedure (4)

(4) Raise the wire with eye splice connected with the messenger rope to upper deck in the bow through the Panama chock by winding the starboard side hawser reel of the port side mooring winch, and stop the winch.  Wind the wire in hawser reel of the port side mooring winch up to the length in which eye splice at the end of the wire can be hooked on the bollard in behind through the bollard in front.

(5) Wind off the hawser from the port side hawser reel of the port side mooring winch and connect it to the wire with eye splice through the roller fairleader by using the strop chain.

(6) Wind up the hawser in the port side hawser reel of the port side mooring winch and keep the tension on the middle of the wire with eye splice.

(7) Wind off the starboard side hawser reel of the port side mooring winch and separate the wire with eye splice from the messenger wire.

Procedure (5) & (6)

Procedure (7)

(8) Hook the eye splice at the end of the wire on the bollard in behind after winding the wire around the bollard in front once.

(9) Wind off the port side hawser reel of the port side mooring winch and detach the strop chain from the wire with eye splice.

Procedure (8)

Procedure (9)

(1) Wind off the hawsers from both the starboard side hawser reel of the port side mooring winch and the port side hawser reel of the starboard side mooring winch.

(2) Receive the messenger ropes from the towing ship.

(3) Connect the messenger ropes to the starboard side hawser and the port side hawser of the mooring winch through the fairleaders and the bollards on both side.

(4) Raise the wires with eye splice connected with the messenger ropes to the towing ship through the bollards and fairleaders on both side by winding off the both side hawser reels of the mooring winches, and stop the winches after the hawsers are fixed to the towing ship.

Procedure (1), (2) & (3)

Procedure (4)

2nd engineer

Crews and bosun carry portable wireless radio.

Fireman B

Fireman C

Fireman A

Seaman C

Seaman B

(assist)

2nd officer

Quartermaster

3rd officer

(Onboard wireless radio)

(International VHF16ch)

Chief officer

Captain

Bridge

Towing ship

Seaman A (handling mooring winch)

Bosun

On upper deck in bow (on upper deck in stern)